## Slide 1: Chapter 2
Radio and Signals Fundamentals
Name, Callsign
Discussion Leader
American Radio Relay League
Notes: 333

## Slide 2: Brief Review of Chapter 3 Exam Questions
What is the electrical term for the electromotive force (EMF) that causes electron flow?
Voltage
Ampere-hours
Capacitance
Inductance
2019 MDARC Technician License Course
2

## Slide 3: Brief Review of Chapter 3 Exam Questions
What is the electrical term for the electromotive force (EMF) that causes electron flow?
Voltage
T5A05 Page 3-2
3
2019 MDARC Technician License Course

## Slide 4: Brief Review of Chapter 3 Exam Questions
What formula is used to calculate current in a circuit?
Current (I) equals voltage (E) multiplied by resistance (R)
Current (I) equals voltage (E) divided by resistance (R)
Current (I) equals voltage (E) added to resistance (R)
Current (I) equals voltage (E) minus resistance (R)
4
2019 MDARC Technician License Course

## Slide 5: Brief Review of Chapter 3 Exam Questions
What formula is used to calculate current in a circuit?
Current (I) equals voltage (E) divided by resistance (R)
T5D01 Page 3-5
I=E/R
Look familiar?
5
2019 MDARC Technician License Course

## Slide 6: Brief Review of Chapter 3 Exam Questions
What component is commonly used to change 120V AC house current to a lower AC voltage for other uses?
Variable capacitor
Transformer
Transistor
Diode
6
2019 MDARC Technician License Course

## Slide 7: Brief Review of Chapter 3 Exam Questions
What component is commonly used to change 120V AC house current to a lower AC voltage for other uses?
Transformer
T6D06 Page 3-9
7
2019 MDARC Technician License Course

## Slide 8: Chapter 2 Radio and Signals Fundamentals
In this session we will see electricity at work to generate radio signals.
8
2019 MDARC Technician License Course

## Slide 9: Chapter 2 2.1 Radio Signals and Waves
  Radio Signals are composed of radio waves that travel at the speed of light.
    When Hams talk about signals, they are referring to the electrical energy they use to exchange information inside or out of a radio.
9
2019 MDARC Technician License Course

## Slide 10: Chapter 2 2.1 Radio Signals and Waves
  Radio waves start in an antenna as an electrical signal that constantly reverses direction.
  The rate at which the signal changes direction--backward and forward-- is the signal’s frequency.
  The radio waves radiate from the antenna and vibrate or oscillate at the same frequency as the electrical signal.
  As the radio wave passes other antennas, it creates replicas of the original electrical signal.
10
2019 MDARC Technician License Course

## Slide 11: Chapter 2 2.1 Radio Signals and Waves
  Radio waves from transmitter to receiver
Information (voice, data, video, commands, etc.) is converted to electronic form.
The information in electronic form is added to a radio wave.
The radio wave carrying the information is sent from the station antenna into space.
11
2019 MDARC Technician License Course

## Slide 12: Chapter 2 2.1 Radio Signals and Waves
  Radio wave from transmitter to receiver
The radio waves carry the information.
The receiver extracts the information from the received wave.
The information is then presented to the user in a format that can be understood (sound, picture, words on a computer screen, response to a command, etc.)
2019 MDARC Technician License Course
12

## Slide 13: Chapter 2 2.1 Radio Signals and Waves
  Frequency, Amplitude and Phase
  Frequency is the number of complete cycles of an alternating current or alternating voltage that occur per second.
13
2019 MDARC Technician License Course
Frequency Similar to Figures 2.1 and 2.2

## Slide 14: Chapter 2 2.1 Radio Signals and Waves
  Frequency, Amplitude and Phase
  Amplitude is the strength or magnitude of a signal.
14
2019 MDARC Technician License Course
Frequency Similar to Figures 2.1 and 2.2

## Slide 15: Chapter 2 2.1 Radio Signals and Waves
  Frequency, Amplitude and Phase
  Phase is a measure of the position in time within a repeating waveform, such as a sine wave.
15
2019 MDARC Technician License Course

## Slide 16: Chapter 2 2.1 Radio Signals and Waves
  Metric prefixes are commonly used in amateur radio.
The highlighted prefixes are the most frequently used in amateur radio.
Expansion of Table 2.1
16
2019 MDARC Technician License Course

## Slide 17: Chapter 2 2.1 Radio Signals and Waves
  The Radio Spectrum
    Radio Spectrum is the term used to refer to the vast array of available radio frequencies.
    Audio Frequencies (AF) are signals below 20 kHz that humans can hear.
    Radio Frequencies (RF) are signals above 20kHz.
17
2019 MDARC Technician License Course

## Slide 18: Chapter 2 2.1 Radio Signals and Waves
  The Radio Spectrum
Similar to Table 2-2
Remember that 1 MHz = 1000 kHz; 1 GHz = 1000 MHz
18
2019 MDARC Technician License Course

## Slide 19: Chapter 2 2.1 Radio Signals and Waves
  The part of the electromagnetic spectrum composed of radio waves is called the radio frequency or Radio Frequency Spectrum.
Figure 2.3
19
2019 MDARC Technician License Course

## Slide 20: Chapter 2 2.1 Radio Signals and Waves
Wavelength is the distance a radio wave travels during one cycle of the wave’s electric and magnetic fields.
Figure 2.5
20
2019 MDARC Technician License Course

## Slide 21: Chapter 2 2.1 Radio Signals and Waves
Since the Wavelength is the distance a radio wave travels during one cycle of the wave’s electric and magnetic fields and the speed of light is constant, here is the formula that relates wavelength and frequency.
300,000,000 meters per second /
Wavelength (λ) in meters = Frequency (f) in hertz or cycles per second
where the Speed of light is 300,000,000 meters per second.
Illustration: What is the wavelength of a 1 MHz radio wave (typical of an AM Broadcast)?
λ = 300 = 300 meters
1
Formula simplification
Wavelength (λ) in meters = 300 /frequency in MHz
21
2019 MDARC Technician License Course

## Slide 22: Chapter 2 2.2 Radio Equipment Basics
A basic radio station is made up of a transmitter and receiver connected to an antenna with a feed line. The transmit-receive (TR) switch allows the transmitter and receiver to share the antenna.
A Transceiver includes the transmitter, receiver and TR switch in a single enclosure
Refer to Figure 2.6
22
2019 MDARC Technician License Course

## Slide 23: Chapter 2 2.2 Radio Equipment Basics
Accessory Radio Equipment
23

## Slide 24: Class Session 6 Assignment
  In preparation for the next class session, do the following…….
  ● Study Chapter 4 “Propagation, Antennas and Feed Lines.”
  ● Study The Chapter 4 Question Pool questions found in the chapter ”blue boxes.”
  See you next week!
24
2019 MDARC Technician License Course

## Slide 25
Please follow the Elmers’ directions